## Slide 1
FORTH Computing on FPGA
Team Members: Jess Totorica, Kyle Hartman, Thys Ballard, Kyle Hild, Ronald Crump
Logic analyzer waveforms were used very regularly to observe the functionality of different design elements. This shows sprite data being loaded from RAM to an internal register to be later drawn to the screen.
FORTH is a very small programming language that was originally developed for controlling scientific instrumentation.
A custom designed soft-CPU that executes FORTH instructions on an FPGA is a very versatile, low power, and small form factor way to accomplish many computing tasks.
Our design, called the F18, is ideal for applications with many arithmetic calculations, high data throughput, or as a controller for designs with other subsystems.
Develop an Arduino-like board/platform based upon an FPGA executing FORTH bytecode instructions.
Objective
Background
Several development boards were used for this project, with the Alorium Hinj being the final choice due to the convenient features and easy expansion.
The J1, an FPGA based Forth CPU created by James Bowman, served as inspiration for the project.
Concept Development
Testing and Validation
Designed specifically for running FORTH
Two RAM based LIFO stacks
  Data Stack: Data manipulation and calculation
  Return Stack: Stores return address for function calls
18-bit instruction width, 16-bit data paths
Uses true dual port SRAM for data and program storage
16 MHz clock
System Input/Output
UART (Universal Asynchronous Trans./Rec.
  Allows for serial communication with external devices
VGA (Video Graphics Array)
  Allows for display on VGA monitor
  Specifically designed for displaying Pong game
GPIO (General Purpose I/O)
  Allows for input and output to/from physical pins on board
CSR (Control/Status Registers)
  Coordinates data flow between I/O peripherals and F18 processor
F18 Processor
Final Design
Going Forward
Acknowledgements
Thanks to Peter Baran for being a sponsor, mentor and teacher. Thanks to Mark Sapper for his help with hardware design and debugging. Thanks to James Bowman for allowing us to use his J1 core design. Thanks to Bruce Bolden for being the lead instructor throughout this project.
Develop an Arduino-like board/platform based upon an FPGA executing FORTH bytecode instructions.
-Full ANS FORTH on board
-Arduino like tools/Functions
-Interrupts
-Prototype PCB
Throughout the year this project changed and grew. Our final design met the specifications of a CPU on an FPGA that executes FORTH instructions, and was geared toward running the pong program on the custom F18 processor. Moving forward these are some things we would like to implement and add:
Full ANS FORTH on the board
Arduino like tools/functions
Hardware interrupts
Prototype custom PCB